## Slide 1
6 Credits
Project ID – W27
HOME
AUTOMATION
USING IOT

## Slide 2
TEAM COMPOSITION
ROHAN N KALPAVRUKSHA | PES1201802830 | 
ROSHAN N KALPAVRUKSHA | PES1201802834 | 
AKHIL V NAYANEGALI | PES1201801945 | 
MRIDHULA SRIHARSHA | PES1201801122 | 
GUIDE - Dr. Anuradha M
Professor and Chairperson, ECE Department

## Slide 3
CONTENTS
Introduction
Problem Statement
Block Diagram
Implementation progress
Deliverables
References
Project timeline Gantt Chart

## Slide 4
INTRODUCTION
Home Automation :
  Automatically performs everyday functions around the home
  Saves time, energy, money and provides security.
Internet of Things (IOT) :
  Network of embedded objects
  Connects and exchanges data with other devices over the internet.

## Slide 5
PROBLEM STATEMENT
Brain-numbing task to walk out from our place to control various electric devices
Motivation : Make it self-regulating for physically handicapped and old aged people.
Develop a wrist band to control devices.
Relatively affordable, simple to implement and users friendly.

## Slide 6
IMPLEMENTATION PROGRESS
We have tried to implement the controlling of intensity of bulb with the help of our gesture, voice, slide bar and integrate all three methods.

## Slide 7
BLOCK DIAGRAM
CONTROL DEVICE
(SMART WATCH)
ONLINE DASHBOARD
Speech Sensors
Slide Bar
FAN
LIGHT
CONTROL APP
Node MCU
Arduino IDE
Levels Altered
Wi-Fi
Module
CLOUD

## Slide 8
BLOCK DIAGRAM
FAN
LIGHT
Node MCU
Subscriber
(SMART WATCH)
Node MCU
Publisher
Accelerometer
WI-FI
Senses Gesture
Google
Assistant
Senses Voice
Slide Bar
Senses Movement
MQTT Broker
Publish
Subscribe

## Slide 9
ADVANTAGES OF MQTT
Distribute information more efficiently.
Reduce update rates to seconds.
Very well-suited for remote sensing and control.
Maximize available bandwidth.
Extremely lightweight overhead
Increase scalability.
The real advantage of MQTT over HTTP occurs when we reuse the single connection for sending multiple messages in which the average response per message converges to around 40 ms and the data amount per message converges to around 400 bytes.

## Slide 10
CIRCUIT
SETUP NEAR BULB
SETUP NEAR
SMART WATCH

## Slide 11
VOICE CONTROL
Hey Google, Turn on Bulb at 30 %

## Slide 12
VIDEO

## Slide 13
DELIVERABLES
A smart Wristband to control the functions of the
light bulb and fan through slide bar, voice and gesture.
Technical paper writing.
Phase 1
Phase 2
Controlling of led through a Slide Bar using Blynk App

## Slide 14
REFERENCES
[1]Assad Mohammed , Amar Seeam , Xavier Bellekens z, Kamila Nieradzinska x, Visham Ramsurrun , “Gesture based IoT Light Control for Smart Clothing” , 2016 IEEE International Conference on Emerging Technologies and Innovative Business Practices for the Transformation of Societies (EmergiTech), Avaliable online: 10.1109/EmergiTech.2016.7737326
[2] Sajid Nagarboudi Patel a, R.D.Salagarb ,”A Review on Iot Light Control for Smart Clothing using Gesture Control”
International Journal of Innovative and Emerging Research in Engineering Volume 4, Issue 6, 2017.
[3] Yash Govilkar, Dr. Rupesh Jaiswal , “A Gesture Based Home Automation System” , International Journal for Research in Applied Science & Engineering Technology (IJRASET), Volume 7 Issue XI, Nov 2019, Available online: http://doi.org/10.22214/ijraset.2019.11081
[4] Osheen Bindroo, Komal Saxena, Sunil Kumar Khatri, “A Wearable NFC Wristband for Remote Home Automation System”, 2017 2nd International Conference on Telecommunication and Networks (TEL-NET), Available Online :10.1109/TEL-NET.2017.8343563
[5] Ravi Kishore Kodali, Borra Yatish Krishna Yogi, Gudibanda Nagesh Sharan Sai, Jehova Honey Domma, “Implementation of Home Automation Using CoAP”, 28-31 Oct. 2018 TENCON 2018 - 2018 IEEE Region 10 Conference
[6] Kamelya Dehghani Kohnehshahri, Mohammad Hasan Kargar, Fatemeh Soleimani-Roozbahani, “The Effect of Using COAP Protocol on Reducing Energy Consumption in Smart Houses”, Sep 8, 2018 Int. J. Advanced Networking and Applications Volume: 10Issue: 03Pages: 3843-3852 (2018) ISSN: 0975-0290

## Slide 15
PROJECT TIMELINE (PHASE 2)
SCHEDULE | JUNE | JULY | AUGUST | SEPTEMBER
IMPLEMENTATION OF ALGORITHM TO DETECT THE GESTURE |  |  |  | 
DEVELOPMENT OF GESTURE DETECTION SYSTEM |  |  |  | 
INTEGRATE ALL THREE TECHNIQUE TO CONTROL BULB |  |  |  | 
IMPLEMENTING THE CIRCUIT FOR FAN & DESIGN OF THE WRISTBAND |  |  |  | 
FINAL REPORT AND TECHNICAL PAPER WRITING |  |  |  | 

## Slide 16
THANK YOU